## Slide 1: NeuroDOT
Tutorial:
Data Pre-processing

## Slide 2: Diffuse Optical Tomography
In diffuse optical tomography (DOT), arrays of optical sources and detectors are used to perform functional neuroimaging experiments on task-based or resting state modes of human brain function.
Analyses are broken into several pipelines:
  B: modeling of the tissue and optical geometry
  C: modeling of the light emission, diffusion, and detection through the head
  D: preprocessing of the raw source-detector measurements
  E: reconstruction and spectroscopy of the preprocessed data and light model into a functional neuroimaging volume
  F: post-processing analysis of these results.

## Slide 3: Pre-processing
This tutorial will follow the Script_TBN.m Matlab file which can be found in the Documentation/Scripts folder.
In this tutorial, you will:
  Generate data quality assessment figures
  Process and visualize raw source-detector measurements
    Examine different ‘nearest neighbor’ measurements, with varying source-detector distance
    Examine the measurement spectrum
    Explore effects of filter cutoff frequencies
    Examine effects of superficial signal regression
We will use data from a rotating-wedge retinotopy experiment
Start by loading this data set:
load('NeuroDOT_Base_CCW_Sample1.mat'); % data, info, flags

## Slide 4: Data Quality Assessment – Time Traces
The left panels show data at 750 nm and the right panels show data at 850 nm.
The top panels show all measurements and the bottom panels measurements with standard deviation below a set threshold
The y-axis on all is log scale to highlight the range of light levels for the set of source-detector distances.
Vertical lines on the bottom row of plots signify time points where something happened in the stimulus paradigm.
Plot_RawData_Time_Traces_Overview(data,info);

## Slide 5: Data Quality Assessment – Time trace Summary Plots
(Upper left) A zoomed-in view of several signals shows the presence of cardiac pulse at approximately 1 Hz
(Lower left) Spectral measures averaged over several time traces show strong peaks at 1Hz (cardiac pulse) and approximately 1/26 Hz (the stimulus frequency)
(Upper right) Light level (log) vs. source-detector distance shows expected falloff, with cross-talk at distances > 45 mm
(Lower right) Histogram of signal % standard deviation shows several measurements below ‘good measurement’ threshold
Plot_RawData_Metrics_I_DQC(data,info)
[Figure to be modified to show (up left) time-trace zoom, (low left) Average signal spectrum, (up right) light level falloff vs. s-d distance (low right) histogram of signal % stdev]

## Slide 6: Data Quality Assessment – Cap Fit Summary
Top row shows average light levels for short-distance (left) and medium-distance (right) measurements. Good coupling across the entire cap results in mostly white and yellow in these figures.
Middle row show signal-to-noise ratio (SNR) for cardiac pulse band of frequencies.
Bottom edge plot shows measurements that satisfy the criteria. Optodes that have multiple ‘bad’ measurements are identified with large circles.
Plot_RawData_Cap_DQC(data,info);

## Slide 7: Pre-processing of Raw Measurements
Pre-processing generally follows the pipeline on the right, as in this section of code:
  lmdata = logmean(data); % Logmean Light Levels
  info = FindGoodMeas(lmdata, info, 0.075); % Detect Noisy Channels
  ddata = detrend_tts(lmdata); % Detrend Data
  hpdata = highpass(lmdata, .02, info.system.framerate); % High Pass Filter
  lp1data = lowpass(hpdata, 1, info.system.framerate); % Low Pass Filter 1
  hem = gethem(lp1data, info); % Superficial Signal Regression
  [SSRdata, ~] = regcorr(lp1data, info, hem);
  lp2data = lowpass(SSRdata, 0.5, info.system.framerate); % Low Pass Filter 2
  [rdata, info] = resample_tts(lp2data, info, 1, 1e-5); % 1 Hz Resampling
  % Block Averaging
  badata = BlockAverage(rdata, info.paradigm.synchpts(info.paradigm.Pulse_2), 30);
The following slides show the data at each of these stages to demonstrate the effects of pre-processing.
Previous plots of the raw signals used a log-compressed y-axis to display the wide distribution of light levels.
Subsequent plots and images show differential measurements, computed as the logarithm of the ratio of each signal and its temporal average
DOT Acquisition
Log-mean
Detect noisy channels
Band-pass filter
Superficial signal regression
Resample
Low-pass filter
Reconstruction
Spectroscopy
Spatial normalization
Light
Model

## Slide 8: logmean data
First, take the logmean and find clean measurements (std(logmean)<0.075).
  lmdata = logmean(data); % Logmean Light Levels
  info = FindGoodMeas(lmdata, info, 0.075); % Detect Noisy Channels
The results can be visualized with code such as
  % measurements to include
  keep = info.pairs.WL==2 & info.pairs.r2d < 40 & info.MEAS.GI;
  figure('Position',[300 600 550 780])
  subplot(3,1,1); plot(lmdata(keep,:)')
  xlabel('Time (samples)'), ylabel('log(\phi/\phi_0)')
  subplot(3,1,2); imagesc(lmdata(keep,:))
  colorbar, xlabel('Time (samples)'), ylabel('Measurement #')
  [ftmag,ftdomain] = fft_tts(mean(lmdata(keep,:)',2)',info.system.framerate);
  subplot(3,1,3); semilogx(ftdomain,ftmag)
  xlabel('Frequency (Hz)'), ylabel('|X(f)|'), xlim([1e-3 10])
In a plot (top) of the clean time traces overlain on each other, any response to the stimulus is difficult to discern without additional processing.
In an image view (middle) of all measurements, a possible periodic response to the stimulus may be evident.
A plot of the average spectrum for the wavelength with stronger response (bottom) shows the pulse and stimulus frequencies as before.

## Slide 9: Measurements at Varying Source-detector distance
Viewing measurements from different source-detector distances can help with interpretation
Identify sets of measurements at different distances,
  keepd1 = info.MEAS.GI & info.pairs.r2d<20 & info.pairs.WL==2;
  keepd2 = info.MEAS.GI & info.pairs.r2d>=20 & info.pairs.r2d<30 & info.pairs.WL==2;
  keepd3 = info.MEAS.GI & info.pairs.r2d>=30 & info.pairs.r2d<40 & info.pairs.WL==2;
Plot measurements at each range of distances
  figure('Position',[700 300 1000 700])
  subplot(3,1,1), plot(lmdata(keepd1,:)'), ylabel('R_{sd} < 20 mm')
  subplot(3,1,2), plot(lmdata(keepd2,:)'), ylabel('R_{sd} \in [20 30] mm')
  subplot(3,1,3), plot(lmdata(keepd3,:)'), ylabel('R_{sd} \in [30 40] mm')
  xlabel('Time (samples)')
Displaying the complete time range (top figure, with short-, medium- and long-distance measurements) shows features across the full length of the recording
Reducing the displayed time range (bottom figure) zooms in on features within the data. Here the cardiac pulse (at roughly one cycle per 10 samples, or one second) is prominent
  for i = 1:3, subplot(3,1,i), xlim([2500 2600]), end

## Slide 10: Periodic Waveforms in the Spectrum
The spectrum (right and in a previous slide) is computed with a fast Fourier transform (fft) and shows the presence of periodic, or nearly periodic waveforms in the measurements.
The cardiac pulse shown previously repeats with a period of approximately 1 second and appears as a spike at a frequency of approximately 1Hz
The stimulus in these measurements was a flashing checkerboard wedge rotating once every 36 seconds, so we expect to see it at 1/36 0.028 Hz
Cardiac pulse, ~1Hz
Stimulus frequency, ~0.028Hz

## Slide 11: Detrend and high-pass filter the data
Detrending the data removes a linear trend or drift in each measurement
  ddata = detrend_tts(lmdata); % Detrend Data
Results on this data set are less striking than on other data.
Data are high-pass filtered (cutoff frequency of 0.02 Hz here)
  hpdata = highpass(ddata, .02, info.system.framerate);
The time traces plot shows subtle changes, with a slight flattening over the duration of the measurements
The spectrum (bottom) shows the effect of filtering: frequencies below the cutoff frequency are significantly attenuated (frequencies higher than the cutoff pass through the filter).
Note that the cardiac pulse and stimulus frequencies are still present in the spectrum.

## Slide 12: Detrend and High-Pass
Viewing the filtered measurements from different source-detector distances shows more clearly the significant reduction in low-frequency (over the course of the full measurement duration) changes, especially at the short source-detector distances
The zoomed view shows closer alignment of the short source-detector distance measurements

## Slide 13: Low-pass filter the data
Data are low-pass filtered (1 Hz cutoff frequency)
  lp1data = lowpass(hpdata, 1, info.system.framerate);
The time traces plot shows less high-frequency noise
The image of the measurement time traces now shows a clearer periodic response to the stimulus
The spectrum shows attenuation of frequencies above the cutoff frequency (frequencies lower than the cutoff pass through the filter)

## Slide 14: Low-pass filter zoom
The filtered measurements now show reduced high-frequency (rapidly varying) signal components, apparent at all source-detector distances
The zoomed view shows that the 1Hz cardiac pulse signal is no longer apparent. Accordingly, at the zoomed time scale (10 seconds shown in this plot), very few features of interest are apparent
Variation at the stimulus frequency is not yet clear in the full-length time traces

## Slide 15: Superficial signal regression
A common signal is estimated from the superficial measurements and regressed out of all measurements
  hem = gethem(lp1data, info);
  [SSRdata, ~] = regcorr(lp1data, info, hem);
The time traces plot shows a little less high-frequency noise
The image of the measurement time traces shows an even clearer periodic response to the stimulus
The spectrum shows a much stronger peak at the stimulus frequency relative to other frequencies

## Slide 16: Superficial signal regression
Plot the estimated superficial signal (above)
  figure('Position',[700 600 1000 300])
  plot(hem(2,:))
  title('Estimated common superficial signal')
  xlabel('Time (samples)')
This estimated signal captures features of the previous short-distance measurements
After regression of this estimated signal, short-distance measurements show little structure, while medium- and long-distance measurements show periodic features
After producing the graph at top right, reduce the time range to 3 cycles of the stimulus period, e.g.,
  for i = 1:3, subplot(3,1,i), xlim([1600 1600+360*3]), end
This zoomed view clearly shows three cycles of the stimulus response

## Slide 17: Second LPF and resampling
An additional lowpass filter attenuates frequencies above 0.5 Hz
  lp2data = lowpass(SSRdata, 0.5, info.system.framerate);
Data are then resampled to 1 Hz
  [rdata, info] = resample_tts(lp2data, info, 1, 1e-5);
The 2nd LPF further reduces noise visible in the time traces, showing more emphasis on the stimulus response
Note that there are fewer time samples (reduced by a factor of 10) due to resampling
The spectrum is now displayed only to 1 Hz

## Slide 18: Second LPF and resampling - detail
The second LPF further attenuates rapidly varying (high-frequency) noise
Reducing the filter cutoff frequency from 0.5 Hz to 0.05 Hz drastically reduces the high-frequency noise, leaving only waveforms at the stimulus frequency, but at the expense of altering temporal features of the stimulus response at 0.028 Hz and possibly altering the phase of that response
Cutoff of 0.5 Hz
Cutoff of 0.05 Hz

## Slide 19: Block averaging
The measurements are block-averaged based on the stimulus synchronization points stored in info.paradigm
  badata = BlockAverage(rdata, info.paradigm.synchpts(info.paradigm.Pulse_2), 30);
The time traces now show clear responses to the stimulus, here a rotating flickering checkerboard wedge with the image array over visual cortex.
The measurement image shows spatial variation of the response, as expected as the wedge rotates through the visual field.
More details about the stimulus paradigm and expected responses can be found in Eggebrecht et al., Neuroimage, 2012.
Plotting based on source-detector distance shows that medium- and long-distance measurements comprise nearly all of the strong stimulus responses.